Sf = subflow
Mptcp fast close
TIME_WAIT
M_FASTCLOSE_WAIT
ESTA
M_ESTA_*
CLOSED
M_CLOSED
FIN_WAIT-1
CLOSING
FIN_WAIT-2
SYN_RCVD
LAST-ACK
SYN_SENT
CLOSE WAIT
TIME WAIT
LISTEN
Force CLOSE
Send RST and then tears down all but one subflows
Send MP_FASTCLOSE on remaining sf
Recv TCP RST on remaining sf
Recv MP_FASTCLOSE (1)
Send RST backwards
Tears down all subflows
Recv MP_FASTCLOSE (1)
Send RST
Tear down connection
[Speaker Notes: Should note conditions such as */**/*** ; (1) on valid key Figure 17 of RFC 6824 shows the FSM for closing a connection - An mptcp connection can have 0 subflows. -]

---
Connection establishment (master subflow)
2 Cases : additional subflows exist/only one.
En M_ESTAB_1 on peut créer
M_ESTAB_WAIT
(waits for a DSS to be DATAACKED)
ESTAB
(Fallback to TCP)
M_ESTAB_MP
(can establish new subflows)
Recv ACK only
Sends DSS Infinite mapping
Recv DataAck
Recv SYN/ACK + MP_CAPABLE
Send ACK + MP_CAPABLE
Recv SYN + MP_CAPABLE
Send Syn/ACK + MP_CAPABLE
Recv SYN/ACK
Send ACK
Detects failure
Sends
[Speaker Notes: There is, however, another corner case that should be addressed. That is one of MPTCP options getting through on the SYN, but not on regular packets. This can be resolved if the subflow is the first subflow, and thus all data in flight is contiguous, using the following rules. A sender MUST include a DSS option with data sequence mapping in every segment until one of the sent segments has been acknowledged with a DSS option containing a Data ACK. Upon reception of the acknowledgment, the sender has the confirmation that the DSS option passes in both directions and may choose to send fewer DSS options than once per segment.]

---
Master subflow connection
CLOSE
LISTEN
M_LISTEN
M_SYN_RCVD
M_SYN_SENT
M_ESTAB_WAIT
(waiting for a DSS to be DATAACKED)
M_ESTAB_MP_1
(can establish new subflows &
send mappings for multiple segments)
M_ESTAB_SP
(Fallback to TCP)
Recv SYN/ACK + MP_CAPABLE
Send ACK + MP_CAPABLE
Recv ACK + MP_CAPABLE
Sends Data Ack
Recv ACK only
Recv DataAck
Open
Send SYN+MP_CAPABLE
Recv SYN + MP_CAPABLE
Send Syn/ACK + MP_CAPABLE
Recv SYN/ACK
Send ACK

---
Connection (subflow) join
CLOSE
M_ESTA_MP_* (* = 1 or 2)
LISTEN (?)
M_ESTA_MP_*
M_SYN_RCVD
M_ESTA_MP_*
M_ESTA_MP_2
FINWAIT-1
M_ESTAB_MP_* ( ? ou bien encore 2)
M_ESTAB_MP_*
Recv SYN/ACK + MP_JOIN
Sends ACK + MP_JOIN
Recv ACK + MP_JOIN
Failure detected
Sends RST + MP_FAIL
Close subflow
Sends FIN
Sends
Open new subflow
Send SYN+MP_CAPABLE
Recv SYN + MP_JOIN
Sends SYN/ACK + MP_JOIN

---
Subflow closing (several subflows)
M_ESTA_MP_2
See Legacy TCP FSM
Failure detected
Recv DATAFIN

---
Subflow closing (1 subflow)
M_ESTA_MP_1
Data contiguous
Cf FSM of RFC6824
Appendix C
Figure 17
See Legacy TCP FSM
M_ESTA_MP_1 (or _SP?) if
Creates new subflow
Else
Failure detected (ie wrong checksum)
Sends MP_FAIL
Recv DATAFIN
Yes
=>
Recv MP_FAIL
No =>